## Slide 1: Artificial Neural Network (Back-propagation)
Hardware implementation models

## Slide 2: Verilog model (sync reset)
Area cost:
  Slide LUTs: 2627
  Slice Registers: 1862
  Mux: 60
  Memory: 1 ROM 256x16 (sigmoid)
  DSP: 53
  IO: 68
Timing:
  Setup: 0.754ns
  Hold: 0.072ns
Others:
  Error_output use multiplier DSP mapping (4 times)
Features:
  Fixed parameters
  Synchronous reset signal

## Slide 3: VHDL model (ver1.0)
Area cost:
  Slide LUTs: 1326
  Slice Registers: 1286
  Mux: 85
  Memory: 6 ROM 256x16 (sigmoid)
  DSP: 60
  IO: 101
Timing:
  Setup: -0.466ns
  Hold: 0.113ns
Others:
  Error_output NOT used multiplier DSP
  Forward, derivative_activation, delta_weight_cumulation, delta_bias_cumulation use multiplier DSP mapping.
Features:
  Reconfiguration parameters
  Asynchronous reset signal (for optimizing fpga)

## Slide 4: VHDL model (ver1.2)
Area cost:
  Slide LUTs: 1464
  Slice Registers: 1978
  Mux: 85
  Memory: 6 ROM 256x16 (sigmoid)
  DSP: 60
  IO: 101
Timing:
  Setup: 0.565ns
  Hold: 0.093ns
Others:
  Error_output NOT used multiplier DSP
  Forward, derivative_activation, delta_weight_cumulation, delta_bias_cumulation use multiplier DSP mapping.
Features:
  Reconfiguration parameters
  Synchronous reset signal (same as verilog)